## Slide 1
INITIAL 1-D SINGLE PHASE LIQUID VERIFICATION OF CTF
Chris Dances
Mentor: Dr. Vince Mousseau
Advisors: Dr. Kostadin Ivanov & Dr. Maria Avramova
Objective: To perform an initial verification study of CTF
Conclusions and Future Work
Introduction
Richardson Extrapolation
CTF is a FORTRAN based code solves 8 conservation equations for liquid, entrained droplet, and vapor phases phases, plus one conservation equation for non-condensable gases. A 1-D residual formulation of the code has been created. While other residual formulations have been formed for other versions of COBRATF [2], none have been integrated into the CASL version of CTF. The current version of CTF has standard verification practices that focus on software quality engineering similar to those in other versions of COBRA-TF [3], but lacks an in depth verification document that focuses on numerical algorithm verification. This paper focuses on this second type of verification and outlines the initial verification of the original version of the code as well as the residual version of the code. The verification problem is a single phase 1-D channel with transient inlet density and mass flow rate. The problem will undergo a Richardson’s extrapolation in the temporal and spatial domains to verify the convergence and order of accuracy of the error. The study of the order of accuracy is considered one of the more rigorous verification criteria [4]. This work will be expanded to perform verification on the single phase equations in both axial and transverse dimensions [5], and coupled fluid heat conduction [6].
Verification Problem Setup
Parameter | Value | Unit
Axial Length | 3.6586 | m
Channel Area | 4.94E-005 | m^2
Wetted Perimeter | 1.49E-002 | m
Velocity | 7.35 | m/sec
Pressure | 155.00 | bar
Temperature 1 | 290.00 | C
Temperature 2 | 295.00 | C
Enthalpy 1 | 1306.3 | kJ/kg
Enthalpy 2 | 1310.9 | kJ/kg
Mass Flow Rate 1 | 0.2707 | kg/sec
Mass Flow Rate 2 | 0.2672 | kg/sec
Final Time | 2.00 | sec
Wave Frequency | 1.00 | Hz
A 1-D single phase channel
Velocity is held constant
Transient Boundary condition
  Mass flow rate
  Enthalpy
Smooth transitions avoid discontinuities
Analytical solution is easily obtained
Python scripting automates input generation, running CTF, and analysis
Spatial
Temporal
The residual formulation of CTF allows for a numerical computation of the multivariable Jacobian matrix compared to the original analytical derivation of a pressure matrix. The 1-D isokinetic single phase liquid verification problem is a good verification problem due its isolation of the order of accuracies through modified equation analysis. The discretization error for both versions of the code converged to zero with decreasing time step and axial mesh size. The order of accuracy for the temporal and spatial refinements matched very closely with the modified equation analysis for both codes. For all of these data points, the residual formulation of the code showed discretization errors that were very close with the original version of the code. Future work should compare the numerical error obtained in the code to the analytical error predicted by the modified equation analysis using the derivatives of the known solutions. While within the asymptotic range, the first order accurate analytical error should almost exactly match the error from the code.
Time step size reduce by half
Observed error converges to zero
Calculated order of accuracy converges to 1
Mesh size reduced by half
Observed error converges to zero
Calculated order of accuracy converges to 1
Verification Results
The numerical error will propagate through the solution resulting in more error at the outlet
The expected error can be computed from the known solution, and compared to the observed
The expected error is local, and was found to scale by dimensionless length
Scaled expected error matches closely with observed error while in asymptotic range